## Slide 1: Weekly Progress
Master thesis
Gabriel Vallat

## Slide 2: 27/09/22
Summary:
Stability as a DCSP
Graphical interface
Problem set-up

## Slide 3: Stability as a DCSP
The statics of a 2-dimensional problem is a set of linear inequalities:
  Each non-holded block: add two constraints
  Each interface between two blocks: add two constraints

## Slide 4: Stability as a DCSP
Example:

## Slide 5: Stability as a DCSP
Example:

## Slide 6: Stability as a DCSP
Linear constraints
Can be solved by several algorithms
  Cassowary algorithm:
    Allows to dynamically add and remove constraints.
    Pure python => probably slower
  Gekko:
    Interface building models in binary from the constraints, using different types of solvers
      Would need extensive tests, but probably faster

## Slide 7: Basic plotting capabilities:
A small script allows the plotting of the blocks:

## Slide 8: Problem set-up
The environment will contain:
  R robots:
    Actions can be:
      Release a block:
        Add the constraints regarding a free block to the system
          Sum of forces and torque must be 0
        Remove the constraints regarding the hold block
          Max torque and force applied
      Pick a block from a list and create interfaces at a chosen location in its range
  N blocks:
    A block is defined by 4 corners
    It has a constant density, and its center of mass can then easily be computed
    Each free block add 2 constraints to the static system
    Each hold block add 2 slack constraints
    Each block has at least 1 interface between either the ground or another block

## Slide 9: Problem set-up
The environment will contain:
  I interfaces:
    The interfaces link together the side of a block with a side or corner of another block
    Each interface add either 2 constraints to the system in case of side-side interface, or only 1 in case of side-corner interface
  The list:
    Needed to describe the possible action of the robots.
    Contains a set of possible blocks that the robots can pick from, and the number of remaining block of the corresponding shape
    Ideas:
      The list contains exactly the right number of blocks needed for a structure
      The list contains infinitely many blocks of each type

## Slide 10: Problem setup
R ranges:
  Each robot has only a subset of the plane accessible to lay the blocks
  This range would need to be later better described, and consider the kinematic of the robot as well as the blocks already placed in the structure
  For now, it will simply be a circle, with a fixed radius and centre
  It could later also define the max force and torque appliable.

## Slide 11: Next step:
Start to implement the constraint solver
Look into the creation of interfaces
Look into the handling of collision
Find a way to discretise the action space of the robots:
  How to make it able to find placement like the following:

## Slide 12: 04/10/22
Interface definition
Update in simulation

## Slide 13: Interface definition
3 types:
  Slide
  Lock
  Mixed

## Slide 14: Update in simulation:
A block can be placed using a sliding interface:
Without specifying the free variable
Specifying the free variable (x=0.6)

## Slide 15: Update in simulation:
A block can be placed using a hanging interface:
  This kind of interface would allow to manufacture arbitrary angles
  The intersection of the blocks is much more complicated to find
Without specifying the free variable
Specifying the free variable (x=0.3)

## Slide 16: Adding the block is easy
In this scenario, the blocks come from two types and are added randomly on top of the others

## Slide 17: Adding the block is easy
In this one, square blocks are put on top of one another

## Slide 18: Questions
Should it be possible to remove blocks?
Would the hanging interface be useful
  Same question for the mixed interface
Discretization:
  Clean idea:
    Each action is composed of a sequence of 3 subactions:
      Chose a block from the list
      Chose which face to put against which face
      Chose an offset: A number between 0 and 1, roughly discretized, where 0 means the new block touches an obstacle on the left and 1 means it touches an obstacle on the right
    (Maybe) Problem: reduce the ability to generalize from interface to interface

## Slide 19: Question about the intersection
How to handle these cases:
  Discontinuous valid x

## Slide 20: Next steps
Implementing the intersections of the flat surfaces
Implementing the physics in the simulation

## Slide 21: 11/10/22
Intersection and contact points
Discussion about the action/observation sets

## Slide 22: Contact points

## Slide 23: Contact points
Now the blocks does not overlap when put at random
Takes ~1s to place 100 blocks
  scales in O(n2)
  Without the physics
  Can still be optimized by not checking for intersection with all the blocks

## Slide 24: Action set
Idea: it takes 3 sub-actions to put a block
  Hold or put
  Chose a block
  Chose two faces
  Chose an offset
  Chose if keep holding

## Slide 25: Action set
Idea: it takes 3 sub-actions to put a block
  Start holding
  Chose a block
  Chose two faces
  Chose an offset
  Keep the block
New blocks

## Slide 26: Action set
Idea: it takes 3 sub-actions to put a block
  Chose a block
  Chose two faces
  Chose an offset
New block
0
1
2
3
4
5
6
7
8
0
1
2
3

## Slide 27: Action set
Idea: it takes 3 sub-actions to put a block
  Chose a block
  Chose two (valid?) faces
  Chose an offset
New block
0
1
2
3
4
5
6
7
8
0
1
2
3
9
10

## Slide 28: Action set
Idea: it takes 3 sub-actions to put a block
  Chose a block
  Chose two valid faces
  Chose an offset:
    A number between 0 and 1
X=0

## Slide 29: Action set
Idea: it takes 3 sub-actions to put a block
  Chose a block
  Chose two valid faces
  Chose an offset:
    A number between 0 and 1

## Slide 30: Action set
Idea: it takes 3 sub-actions to put a block
  Chose a block
  Chose two valid faces
  Chose a (valid?) offset:
    A number between 0 and 1
    Without the validity check:
X=1

## Slide 31: Action set
Idea: it takes 3 sub-actions to put a block
  Chose a block
  Chose two valid faces
  Chose a (valid?) offset:
    A number between 0 and 1
    With the validity check:
X=1

## Slide 32: Action set
About the valid offset:
  An interface can have different valid regions
  Leads to discontinuity
X=k
X=k+ε

## Slide 33: Action set
About the valid offset:
  An interface can have different valid regions
  Leads to discontinuity
  If x is to be discretised, might be good to add some inputs:
    Formally:
X=k
X=k+ε

## Slide 34: Action set
Can be stored in a dynamic tree

## Slide 35: Action set: discretised state space
Can use a triangle grid instead:
  Limited in the shapes
  Only 60 or 120 degrees angles are possible

## Slide 36: Observation set
First point: Does the second robot knows if the first one is holding a block?
Two different amount of information:
  Corners
  Corners structured
    (knowing which corner they are connected to)
  Corners + contact points
  Value of the forces applied on a block?

## Slide 37: 18/10/22
Switch to discrete
Triangle grid and possible scenarios
Change in equilibrium calculation

## Slide 38: Switch to discrete
Problems with continuous:
  Describing the actions would have been dynamic and growing linearly with the number of blocks
  Each face would require to test whether or not the last action changed its parameter

## Slide 39: Switch to discrete
Idea: replace the quadrilateral blocks by a grid equilateral triangles
Only possible actions

## Slide 40: Switch to discrete
Extremely fast to rule out impossible move (like leaving the block in the air or putting it at an already occupied place)
Scales with
Example: try to place hexagons at random position (the central one is fixed
  Number of action possible: 2500 (50x50), rotation not allowed
  Time needed to put 500 blocks: 1.84s

## Slide 41: Possible scenarios
Use two types of blocks: hinge and link
Try to build arches with different terrains

## Slide 42: Possible scenarios
Use only hexagonals
Start with a full terrain
Remove blocks so the other robot make the structure collapse

## Slide 43: Equilibrium
Optimization library not usable:
  Time taken to build the model is too long (constant 3s)
  Whereas the solving time is only 0.025s
Try a non-sequential approach with SciPy:
  Works quite well:
    300 blocks at random on a (30x20) grid:
    Take ~53s but
      Put at random
      Much more complicated problem to solve

## Slide 44: Equilibrium results
With the equilibrium test (53s):
Without the equilibrium test (1.38s):

## Slide 45: 25/10/22
Game description

## Slide 46: Game elements
Agents
  Action set
  Observation set
States
  States transition
Reward
Terminal state

## Slide 47: Agents
robots
  Action set:
      : Put and hold
        Let go any block it is holding
        Put a new block
        Hold it
      : Put and Leave
        Let go any block it is holding
        Put a new block
      : Hold
        Go hold an already placed block
      : Leave:
        Let go any block it is holding
      : Remove (optional)
        Remove a block previously placed

## Slide 48: Agents
robots
  Action set:
      or : Put
        Chose a block from a list
        Chose its orientation among 6 choices
        Chose the location of its reference point

## Slide 49: Agents
robots
  Observation set:
    Consider the game as open information:

## Slide 50: States
Grid:
  : coordinates of the leftmost corner of a triangle (using isometric base)
  : (=down) is equal to 0 if the triangle is pointing up, 1 otherwise

## Slide 51: States
States:
  : ids of the block placed at a given coordinates
    -1 if no block are there
    0 if the block is floating (cannot fall and absorbs any force applied to it)
  : ids of the connected ground at these coordinates
    -1 if no blocks are there
  : ids of the robot holding the current coordinates
    -1 if no robot is holding the parts

## Slide 52: State transition
  : Forbidden action. An action that either:
    Place a completely disconnected block
    Place a block at an already used grid-point
    Place a block outside of its range
    Break the physical equilibrium by leaving a block
    If :
      : coordinates of the new block, : id of the new block (-1 if )
    otherwise

## Slide 53: State transition
    If :
      : coordinates of the new block, : id of the smallest connected ground (or -1 if )
    otherwise
    Note that no test is done to separate the region when removing a block.

## Slide 54: State transition
    If :
      : coordinates of the new block (or selected block if ), : id of the robot
    otherwise:

## Slide 55: Terminal state
The game ends when and

## Slide 56: Problem with the setup
Can get into deadlocks:
  Only and are valid for both R1 and R2
  Seems hard to get out of these positions, but always feasible
Held by R1
Held by R2

## Slide 57: Reward function
A prototype of reward function was tested:
    : Reward for connecting two regions
    : Cost of putting a new block
    : Cost of performing a slow action
    : Cost of holding a block
    : Cost of increasing the distance between the connected regions
    : Cost of performing an illegal action

## Slide 58: Advances in simulation:
The discrete simulator is finished:
  Animation is possible (but quite slow)

## Slide 59: Animation

## Slide 60: Next tasks:
Find a (probabilistic) model for state transition:
  Key features:
    On a relatively small grid (10x7) already 420 dimensional states
    Only the hold and connection grids are useful in the cost function, and their values are in the case of a 2 players, 2 region to connect, game
    Action can easily be embedded in a (5x5) array
    Dimensions of a state-action pair: 10’500 integer values
      Need dimensionality reduction
      Maybe transformer-like architecture?
      Or PCA on the visited samples
Implement a modified version of H-MARL

## Slide 61: 31/10/22
New animation
Deep Q learning
Wolpertinger
Feedback on the literature review

## Slide 62: Animation
Two formats:
  HTLM
    link to file
  Gif

## Slide 63: Deep Q learning
Composed of 2 simple parts:
A state encoder:
  Take the grids and transform it into a vector
    For now, it is implemented by a simple convolutional layer, that takes the ups and down as two separate channels
An action-value decoder
  For a given state vector, give the value of each action
The tuples of (state-action-reward-newstate) are not shared between the agents for training

## Slide 64: Deep Q learning
Train off-policy by using a replay buffer
Explore by having an optimistic Q table and choosing its actions by using softmax over them (for now)
Able to find an unforeseen solution:

## Slide 65: Deep Q learning
Implementation:
  Explore by having an optimistic Q table and choosing its actions by using softmax over them
  Chose action as:
    takes a state and return the expected value for each action:
  Train by using stochastic gradient descent:
    Sample transition tuples (state-action-reward-newstate)

## Slide 66: Wolpertinger
Efficient algorithm when a lot of actions are possible
Apparently ~1300 actions is not enough for it to be more efficient than DeepQ
Based on deep deterministic policy gradient and actor critique model
Generate a continuous protoaction and use knn to project it on k real actions, then select one using softmax over these
Still need to figure out the value of several hyperparameters

## Slide 67: Feedback on literature review
a self-supporting structure is an assembly of rigid components that do not require any binder to connect the parts, and that stays in static equilibrium through gravity-induced compression forces that immobilize all the parts
graph of connected blocks
stacking a block on top of another is the same task if the first block is on the ground or already on top of a tower. As this assumption is hardly true in our case
  They only cared about vertical stacking, so the statics of the blocks below the last one can be ignored

## Slide 68: Feedback on literature review
[An agent] knows for sure its own action, and the ones of the other agents [are modelled as stochastics perturbations]
  Central planning and decentralized execution
Q-learning ok for 2 agents
Number of local minima/saddle point increasing? can we them with equations/justification?
Paper from Jan Peters

## Slide 69: Next steps
Small modification on the reward function
  Need to equilibrate the parameters
Finishing the implementation of Wolpertinger:
  Need a good exploration method, as softmax is not enough
Export the gym to a jupyter notebook to better control the experiments

## Slide 70: 15/11/22
State description
Single agent settings
Change in the action space

## Slide 71: State description

## Slide 72: Single agent
A single agent model was implemented
Would ideally be used as a baseline in the long term
Avoid some questions about the rewards strategy for now

## Slide 73: Change in the action space
Changes in the forbidden actions (that break the physical equilibrium):
  Previously:
  Now:
    With a terminal state
  Reason: better exploration of the state space by reducing the time spent in bad situations
The “slow” actions ( and ) were necessary to allow the agents to get out of some dead ends, but can now be ignored in a basic setup

## Slide 74: Change in the action space
Relative vs absolute positioning:
  Absolute positioning:
  Relative positioning:
    Or
Relative is better:
  It scales better
  The same action can be taken twice in a row

## Slide 75: Thoughts about a less sequential Markov game
Until now, the multi-agent setting was done in a sequential way
  Does not utilize fully both the robot capabilities and the Markov game framework
Idea:
  Each agent act simultaneously:
    The physical equilibrium is checked after all the agents performed their actions
  Some actions can force an agent to go in a “busy” state for a few rounds
    Pick a block, dispose of a block, …
Open questions:
  Symmetry of the game: should each agent be treated fairly
  What happens when an action fails

## Slide 76: Thoughts about a more general setup
Until now, the initial state was always the same
Idea:
  Randomly chose the targets to link in the grid
  This would allow a potentially better learning curve (some targets would be easy to reach, some more difficult)